## Slide 1
Kseniia
MINAKOVA
Mykhailo
KIRICHENKO
Roman ZAITSEV
Dmytro
DANYLCHENKO
Stanislav
FEDORCHUK
Welcome
to
Photovoltaic
Universe!

## Slide 3
Solar Panel Construction
The manufacture of a solar mini battery for equipping a maquette of solar tracker was carried out with the desire to repeat the process of manufacturing a real solar battery as much as possible.

## Slide 4
How it’s made
To give hardness to the solar mini battery and protect it from external factors, the SC connected in strings were placed on a base 300*210 mm in size, made of foamed PVC plastic with a thickness of 5 mm.
Also, on the back side of this base were constructive elements for installing the parts of the tracking system.

## Slide 5
How it’s made
The front surface of the solar cell was protected from unfavorable factors, as well as the solar mini-battery was sealed by filling a layer of transparent epoxy resin about 3 mm thick over strings which was placed on the base.
Highly transparent epoxy resin provides good mechanical strength to the entire structure and also minimizes solar radiation loss.
The process of filling the SC strings with epoxy resin was carried out as follows. On the edges of the plastic base, with the help of self-tapping screws, formwork elements made of the same foamed PVC with a thickness of 5 mm and a height of 15 mm were attached, which, when assembled, ensured the presence of a rim sufficient to prevent overflow of epoxy resin during the actual filling and subsequent polymerization.

## Slide 6
How it’s work

## Slide 7
How it’s work